## Slide 1: Code Generation
TeachING Assistant: David Trabish

## Slide 2
MIPS Architecture
MIPS has 32 registers:
  t0, ..., t9
  a0, a1, a3, a4
  v0, v1
  sp, fp
  ra
  …
We will work with MIPS32
  32-bit registers

## Slide 3
MIPS Architecture
Arithmetic instructions operate on registers and constants:
  add, sub, and, mul, div, or, xor, nor, …
li $t0, 3
li $t1, 4
add $t2, $t0, $t1
mul $t3, t1, 7

## Slide 4
MIPS Architecture
Read from memory:
lw $t0,4($t1)
lw $t0,label
lw $t0,label+4
lw $t0,label+8($t1)

## Slide 5
MIPS Architecture
Write to memory:
sw $t0,2($t1)
sw $t0,label
sw $t0,label+4
sw $t0,label+8($t1)

## Slide 6
MIPS Architecture
Branches and Jumps:
beq $t1, $t2, label
bne $t1, 7, label
j label
...
label:

## Slide 7
MIPS Architecture
System calls:
  Syscall number passed via v0
  Arguments are passed via a0, a1, a2, a3
For example, calling PrintInt(17):
li $v0, 1
li $a0, 17
syscall

## Slide 8
Stack Frames
The stack consists of stack frame
Each called function creates it’s stack frame

## Slide 9
Stack
return address
prev base pointer
local var 1
local var 2
argument 1
…
argument 2
…
frame pointer
stack frame
stack grows down

## Slide 10
Stack
int f(int x, int y){
int z = x + y;
return z;
}
int g() {
int x = f(10, 20)
}
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...

## Slide 11
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
sp

## Slide 12
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
argument 2
sp

## Slide 13
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
argument 1
argument 2
sp

## Slide 14
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
argument 1
argument 2
sp

## Slide 15
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
argument 1
argument 2
sp

## Slide 16
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp

## Slide 17
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp
fp

## Slide 18
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp
fp

## Slide 19
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp
fp
prologue

## Slide 20
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp
fp

## Slide 21
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
sp
fp

## Slide 22
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp
fp

## Slide 23
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp
fp

## Slide 24
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp
fp

## Slide 25
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp

## Slide 26
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp

## Slide 27
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp

## Slide 28
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp
epilogue

## Slide 29
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp

## Slide 30
Stack
f:
subu $sp, $sp, 4
sw $ra, 0($sp)
subu $sp, $sp, 4
sw $fp, 0($sp)
move $fp, $sp
sub $sp, $sp, 16
lw $t0, 8($fp)
lw $t1, 12($fp)
add $t2, $t0, $t1
sw $t2, -4($fp)
lw $v0, -4($fp)
move $sp, $fp
lw $fp, 0($sp)
lw $ra, 4($sp)
addu $sp, $sp, 8
jr $ra
g:
...
li $t0, 20
subu $sp, $sp, 4
sw $t0, 0($sp)
li $t0, 10
subu $sp, $sp, 4
sw $t0, 0($sp)
jal f
addu $sp, $sp, 8
move $t0, $v0
...
return address
previous fp
argument 1
argument 2
local var 1
sp

## Slide 31
Translating IR
Our IR is likely to use too many registers
Assume for now, that the number of IR registers is reduced
  Every IR register mapped to a CPU register (t0, … t7)
We will see later how to compute this register allocation

## Slide 32
Translating IR
Translate global variable initializations
Translate the IR instructions for each function
  Implement a translation function for each IR instruction
  If the translation requires additional registers:
    Use s0, s1, …

## Slide 33
Translating IR
Global initializations
init g_1 = 7
init g_s = “1234”
.data:
g_1: .word 7
g_s: .asciiz “1234”
int g_1 = 7;
string g_s = “1234”;

## Slide 34
Translating IR
Assignments (constant)
t1 = c
li $t1, c

## Slide 35
Translating IR
Assignments (read from memory)
For local variables and parameters:
t1 = x
lw $t1, off($fp)

## Slide 36
Translating IR
Assignments (write to memory)
For local variables and parameters:
x = t1
sw $t1, off($fp)

## Slide 37
Translating IR
Assignments (read from memory)
For global variables:
t1 = g_var
g_var: .word 17
...
lw $t1, g_var

## Slide 38
Translating IR
Assignments (write to memory)
For global variables:
g_var = t1
g_var: .word 17
...
sw $t1, g_var

## Slide 39
Translating IR
Arithmetic operation
t0 = add t1, t2
add $t0, $t1, $t2

## Slide 40
Translating IR
Arithmetic operation
t0 = add t1, t2
add $t0, $t1, $t2
ble $t0, max, end
li $t0, max
end:
# more checks…

## Slide 41
Translating IR
Branch
branch_eq t1, t2, label
beq $t1, $t2, label

## Slide 42
Translating IR
Function call
t0 = call f(t1, t2)
sw $t1, 0($sp)
subu $sp, $sp, 4
sw $t2, 0($sp)
subu $sp, $sp, 4
jal f
addu $sp, $sp, 8
move $t0, $v0

## Slide 43
Translating IR
Return (in a function f)
Store result in v0 and jump to f’s epilogue label (f_epilogue)
return t1
move $v0, $t1
j f_epilogue

## Slide 44
Translating IR
Example…
int g = 1;
int f(int x){
int z = x + 1;
return a[z];
}

## Slide 45
Strings
We use null terminated strings
Every character is one byte
string s1 = “1234”;
string s2 = “a”;
...
...
1
2
3
4
\0
a
\0

## Slide 46
Strings
Assume that s1 and s2 are strings
if (s1 == s2) {
}
t1 = s1;
t2 = s2;
t3 = str_eq t1, t2
compare t3, 0
...

## Slide 47
Strings
t1 = s1;
t2 = s2;
t3 = str_eq t1, t2
compare t3, 0
...
lw $t1, -4($fp) // local var 1
lw $t2, -8($fp) // local var 2
li $t3, 1 // result
move $s0, $t1
move $s1, $t2
str_eq_loop:
lb $s2, 0($s0)
lb $s3, 0($s1)
bne $s2, $s3, neq_label
beq $s2, 0, str_eq_end
addu $s0, $s0, 1
addu $s1, $s1, 1
j str_eq_loop
neq_label:
li $t3, 0
str_eq_end:
Inline string comparison

## Slide 48
Strings
t1 = s1;
t2 = s2;
t3 = str_eq t1, t2
compare t3, 0
...
lw $t1, -4($fp) // local var 1
lw $t2, -8($fp) // local var 2
subu $sp, $sp, 4
sw $t2, 0($sp)
subu $sp, $sp, 4
sw $t1, 0($sp)
jal str_eq
addu $sp, $sp, 8
move $t3, $v0
Alternatively, create a function str_eq

## Slide 49
Arrays
Each cell is 4 bytes (int or pointer)
First cell is the size of the array
The rest of the cells contain data
4
11
12
30
31
size
data

## Slide 50
Arrays
Array access
t0 = array_access t1, t2
move $s0, $t2
add $s0, $s0, 1
mult $s0, $s0, 4
addu $s0, $t0, $s0
lw $t0, 0($s0)

## Slide 51
Runtime Errors
Division by zero
t0 = div t1, t2
div $t0, $t1, $t2

## Slide 52
Runtime Errors
Division by zero
t0 = div t1, t2
beq $t2, 0, abort
div $t0, $t1, $t2
...
abort:
li $v0, 10
syscall

## Slide 53
Runtime Errors
Out of bounds array access
t0 = array_access t1, t2
move $s0, $t2
add $s0, $s0, 1
mult $s0, $s0, 4
addu $s0, $t0, $s0
lw $t0, 0($s0)

## Slide 54
Runtime Errors
Out of bounds array access
t0 = array_access t1, t2
bltz $t2, abort
lw $s0, 0($t1)
bge $t2, $s0, abort
move $s0, $t2
add $s0, $s0, 1
mult $s0, $s0, 4
addu $s0, $t0, $s0
lw $t0, 0($s0)
...
abort:
li $v0, 10
syscall

## Slide 55
Runtime Errors
Null pointer dereference
  Arrays
  Field access
  Method calls

## Slide 56
Runtime Errors
Null pointer dereference
For example, in arrays:
t0 = array_access t1, t2
beq $t1, abort
move $s0, $t2
add $s0, $s0, 1
mult $s0, $s0, 4
addu $s0, $t0, $s0
lw $t0, 0($s0)
...
abort:
li $v0, 10
syscall

## Slide 57
Runtime Errors
Null pointer dereference
For example, in field accesses:
t0 = field_access t1, foo
beq $t1, 0, abort
move $t0, off($t1)
...
abort:
li $v0, 10
syscall

## Slide 58: Classes

## Slide 59
Class Layout
class A {
int x;
string y;
int f() { …
int g() { …
}
vt
x
y
f
g

## Slide 60
Class Layout
class A {
int x;
string y;
int f() { …
int g() { …
}
class B extends A {
int z;
int f() { …
int h() { …
}
f
g
h
vt
x
y
z
B’s layout

## Slide 61
Field Access
t0 = field_access t1, f2
move $t0, 8($t1)
vt
f1
f2
…
t1

## Slide 62
Field Access
t0 = field_access t1, f2
beq $t1, 0, abort
move $t0, 8($t1)
...
abort:
li $v0, 10
syscall
vt
f1
f2
…
t1

## Slide 63
Creating Objects
vt_A
f1
f2
…
class A {
int f1;
…
int m1() { …
…
}
A a = new A;
m1
m2
…

## Slide 64
Creating Objects
class A {
int f1 = c;
…
int m1() { …
…
}
A a = new A;
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t
IR

## Slide 65
Creating Objects
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t1
…
.data
vt_A: .word m1, m2, …
m1
m2
…
Virtual Table

## Slide 66
Creating Objects
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t1
…
.data
vt_A: .word m1, m2, …
.text
li $v0, 9
li $a0, size
syscall
move $t0, $v0
m1
m2
…
Virtual Table

## Slide 67
Creating Objects
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t1
…
.data
vt_A: .word m1, m2, …
.text
li $v0, 9
li $a0, size
syscall
move $t0, $v0
la $s0, vt_A
sw $s0, 0($t0)
m1
m2
…
Virtual Table

## Slide 68
Creating Objects
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t1
…
.data
vt_A: .word m1, m2, …
.text
li $v0, 9
li $a0, size
syscall
move $t0, $v0
la $s0, vt_A
sw $s0, 0($t0)
li $t1, c
m1
m2
…
Virtual Table

## Slide 69
Creating Objects
t0 = alloc (size)
set_vt t0, A
t1 = c
field_set t0, f1, t1
…
.data
vt_A: .word m1, m2, …
.text
li $v0, 9
li $a0, size
syscall
move $t0, $v0
la $s0, vt_A
sw $s0, 0($t0)
li $t1, c
sw $t1, 4($t0)
m1
m2
…
Virtual Table

## Slide 70
Method Calls
class A {
int f1 = c;
…
int m1(int x) { …
int m2(int x) { …
}
A a = new A;
z = a.m2(7)
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
IR

## Slide 71
Method Calls
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
m1
m2
…
Virtual Table
subu $sp, $sp, 4
sw $t1, 0($sp)

## Slide 72
Method Calls
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
m1
m2
…
Virtual Table
subu $sp, $sp, 4
sw $t1, 0($sp)
subu $sp, $sp, 4
sw $t0, 0($sp)

## Slide 73
Method Calls
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
m1
m2
…
Virtual Table
subu $sp, $sp, 4
sw $t1, 0($sp)
subu $sp, $sp, 4
sw $t0, 0($sp)
lw $s0, 0($t0)

## Slide 74
Method Calls
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
m1
m2
…
Virtual Table
subu $sp, $sp, 4
sw $t1, 0($sp)
subu $sp, $sp, 4
sw $t0, 0($sp)
lw $s0, 0($t0)
lw $s1, 4($s0)

## Slide 75
Method Calls
t0 = a
t1 = 7
t2 = virtual_call t0, m2, t1
z = t2
m1
m2
…
Virtual Table
subu $sp, $sp, 4
sw $t1, 0($sp)
subu $sp, $sp, 4
sw $t0, 0($sp)
lw $s0, 0($t0)
lw $s1, 4($s0)
jalr $s1
addu $sp, $sp, 8

## Slide 76
SPIM
.data
g_foo: .word 17
g_str: .asciiz “hello”
…
.text
li $v0, 1
lw $a0, 17
syscall
li $v0, 4
li $a0, g_str
syscall
PrintInt(17)
PrintStr(“hello”)
global data
code

## Slide 77
SPIM
Runing SPIM:
  spim –f input_file
Interactive debugging:
  xspim
Tutorials:
  https://courses.cs.washington.edu/courses/cse410/08sp/notes/spim/SpimTutorial.pdf
  https://web.stanford.edu/class/cs143/materials/SPIM_Manual.pdf